# Home Automation with Tasmota
## General
There are some general commands and features that Tasmota provides to make working with the devices easier.
## Groups
Using groups allows you the capability of sending the same command to multiple devices. For instance it is possible to turn on or off all of the Tasmota enabled devices by sending an MQTT command. Here are some examples:
turn on all devices
cmnd/sonoffs/power1 1
get current state of all devices (an invalid payload causes all devices to return their current state)
cmnd/sonoffs/power1 check
change the ssid and password on all devices
Backlog ssid1 <myssid>; password1 <mypassword>

## Garage Controller
### Introduction
In order to use a Sonoff type device as a garage door controller you must be able to provide a dry contact and have that dry contact close for approximately 1 second. This will instruct the garage door opener to open or close the garage door.
### Hardware
A regular sonoff basic can be modified to provide a dry contact by cutting the traces on the PCB that provides power to the contacts of the relay. This is tricky but possible. The better solution is to purchase a Sonoff SV (safe voltage).
The sonoff basic in the garage has a DHT22 connected to provide a temperature and humidy. It should be noted that the DHT22 and the AM2301 are equivalent.
### Software
The software is the regular version of Tasmota (sonoff.bin).
### Configuration
The sonoff basic is setup as follows:
Channel	Description	Setting
GPIO1	Serial Out	Switch2 (10)
GPIO2	N/A	None (00)
GPIO3	Serial In	Switch3 (11)
GPIO4	N/A	None (00)
GPIO14	Sensor	AM2301 (02)

PulseTime
The pulse time command is used to ensure the relay is only on for a specified duration. In the case of the garage door opener this time is 1 second. The pulse time value is set in units of 0.1 seconds. To set the pulse time enter the following at the console:
PulseTime 10
Door Status
The open and closed statuses are connected to the GPIO1 and GPIO3 inputs. These signals are dry contacts that are closed when the sensor is near. This means that when the door is “closed” the closed signal will show Off and the open signal will show On. The opposite is true when the door is “open”.
MQTT
The data is transmitted via MQTT. The topic is set to “garage”. Under the Logging configuration the telemetry period must be set to 10. This ensures that the MQTT messages are transmitted at a faster rate (every 10 seconds).

## Bathroom Fan Control
### Introduction
The bathroom fan control uses a wifi enabled smart switch running the Tasmota firmware. The switch replaces the standard switch that controls power to the fan. The smart switch is connected to an AM2301 temperature/humidity sensor. Currently the logic for controlling the fan is run by NodeRed although this could be reconfigured to use rules running within Tasmota to remove the need for NodeRed.
Using Tasmota Rules feature it would be possible to move all logic for control into the smart switch. This would allow control even if communication with the MQTT broker was down.
### Hardware
The wifi switch has a DHT22 connected to provide a temperature and humidy. It should be noted that the DHT22 and the AM2301 are equivalent.
### Software
The software is the regular version of Tasmota (sonoff.bin).
### Configuration
The sonoff basic is setup as follows:
Channel	Description	Setting
GPIO1	Serial Out	AM2301 (02)
GPIO2	N/A	None (00)
GPIO3	Serial In	None (00)
GPIO4	N/A	None (00)
GPIO14	Sensor	None (00)

PulseTime
The pulse time command is used to ensure the relay is only on for a specified duration. In the case of the garage door opener this time is 1 second. The pulse time value is set in units of 0.1 seconds. To set the pulse time enter the following at the console:
PulseTime 10
MQTT
The data is transmitted via MQTT. The topic is set to “dn_bath”. Under the Logging configuration the telemetry period must be set to 60. This ensures that the MQTT messages are transmitted at a faster rate (every 60 seconds).
Local Control Logic
If performing the control within the smart switch was desired a Rule could be setup to provide this functionality.
rule1 on AM2301#Humidity>90 do Power1 1 endon on AM2301#Humidity<85 do Power1 0 endon
rule1 1

## Three Way Switch Control
### Introduction
The three way switch control uses two wifi enabled smart switches running the Tasmota firmware. One switch replaces the standard switch that controls the light while the other switch is independent and can be installed anywhere. The Tasmota Rules feature is used to provide all of the logic for control and is integrated into the smart switch. This allows control even if communication with the MQTT broker was down.
### Hardware
A standard wifi switch is used without any additional sensors.
### Software
The software is the regular version of Tasmota (sonoff.bin).
### Configuration
The sonoff basic is setup as follows:
Channel	Description	Setting
GPIO1	Serial Out	None (00)
GPIO2	N/A	None (00)
GPIO3	Serial In	None (00)
GPIO4	N/A	None (00)
GPIO14	Sensor	None (00)

MQTT
The data is transmitted via MQTT. The topic is set according to the location of the switch. Under the Logging configuration the telemetry period must be set to 60. This ensures that the MQTT messages are transmitted at a faster rate (every 60 seconds).
Local Control Logic
In order for the two switches to communicate each switch must be setup independently.
Master Switch (the one connected to the light)
The rule is used to set the state of the secondary switch to match the primary switch. Each time the primary switch state changes the message is published. This ensures the two state of the two switches remain in sync.
rule1 on power1#state do publish cmnd/<secondary topic>POWER %value% endon
rule1 1
Slave Switch (the one not connected to the light)
The rule is used to command the primary switch to toggle it’s state. If the primary switch is on it will turn off and vice versa.
rule1 on button1#state do publish cmnd/<primary topic>/POWER TOGGLE endon
rule1 1